## Slide 1
EMBEDDED SYSTEMS WORKSHOP
Aerial Manipulation
AI-Enabled Perception & 3D Grasping Pipeline on the Qualcomm QIDK Platform
PROJECT MEMBERS
S.L.A. Kartikeya • N.L. Sankeerth • Pranathi Giri • Yashitha Chennupati
Prof: Spandan Roy | Mentor: Sarthak Mishra | TA: Aryama Murthy

## Slide 2
PROJECT OVERVIEW
Problem Statement
Optimizing multi-task robotic vision under strict aerial edge constraints
2 / 18
CORE OBJECTIVE
Build an optimized, real-time software pipeline integrating depth analysis, segmentation, 3D grasping, and pose calculation onboard the Qualcomm QIDK platform.
01 • SWaP & EDGE COMPUTE
Severe Aerial Resource Limits
• Strict Power Envelope: UAV battery limitations mandate ultra-low wattage compute (<15W) with zero thermal throttling.
• Fully Onboard Autonomy: Must process raw camera feeds on Qualcomm QIDK without ground-station offload dependencies.
• Memory Bandwidth Limits: Concurrent deep neural networks compete for shared edge SoC memory bus.
02 • LATENCY BOTTLENECK
Multi-Task Vision Lag
• Cumulative Delays: Running Depth, Segmentation, and Pose sequentially accumulates frame lags (>150ms), destabilizing flight control.
• Throughput Requirement: Grasping moving/hovering targets requires deterministic real-time processing (>30 FPS).
• Heterogeneous Scheduling: Demands balanced pipelining across Kryo CPU, Adreno GPU, and Hexagon NPU.
03 • AERIAL DYNAMICS
Dynamic Flight Perturbations
• Hover Jitter & Vibration: Rotor oscillations and aerodynamic wash introduce high visual blur and camera parallax.
• Spatial Grasp Precision: Requires millimeter-level 3D grasp coordinates despite target and drone movement.
• Continuous Re-planning: Pose estimates must update dynamically as the robotic end-effector nears contact.

## Slide 3
CONTEXT & SIGNIFICANCE
Project Motivation
Transforming UAVs from passive observers to interactive physical agents
3 / 18
PARADIGM SHIFT
From Passive Sensing to Physical Interaction
• Beyond Observation: Conventional drones are strictly limited to inspection and photography. Aerial manipulation empowers drones to physically interact with their environment.
• High-Impact Applications: Enables remote valve turning in refineries, hazardous waste retrieval, search-and-rescue payload delivery, and structural repair.
• Complex Manipulator Mechanics: Requires closed-loop coordination between aerial flight dynamics and lightweight multi-DoF robotic arms.
AUTONOMY REQUIREMENT
Necessity of Zero-Lag Onboard Intelligence
• Fragility of Teleoperation: RF links in industrial or disaster zones suffer from signal shadowing, high packet jitter, and total dropouts.
• Safety-Critical Dynamics: Physical contact with objects exerts reaction forces on the drone. A 100ms latency spike can cause immediate flight instability or crashes.
• Closed-Loop Control: Perception must run at camera frame rate (>30 FPS) to feed visual servoing algorithms without lag.
HARDWARE ENABLER
The Qualcomm QIDK Platform Advantage
• Heterogeneous Compute: Combines high-performance Qualcomm Kryo CPU, Adreno GPU, and Hexagon NPU with dedicated vector/tensor accelerators.
• Qualcomm AI Hub: Provides pre-compiled, optimized neural backbones with hardware-specific INT8/FP16 quantization.
• Optimal Energy Efficiency: Achieves peak deep learning TOPS per watt, preserving flight battery longevity and payload flight endurance.

## Slide 4
SYSTEM ARCHITECTURE
Proposed Solution: Modular Vision Pipeline
Decoupled multi-stage architecture with independent execution nodes
4 / 18
ARCHITECTURAL PRINCIPLE: Complete decoupling of all stages communicating via zero-copy inter-process communication.
STAGE 1
Image Capture
• Camera Interface: MIPI-CSI / USB3 camera driver at 60 FPS.
• Pre-processing: Hardware ISP debayering, undistortion & rectification.
• Buffer Dispatch: Feeds shared memory ring buffer for parallel consumer nodes.
→
STAGE 2
Depth Calculation
• Neural Monocular: Real-time depth estimation using FastDepth / MiDaS.
• Metric Scaling: Computes dense distance maps for metric Z coordinates.
• Obstacle Map: Assists collision clearance during manipulator approach.
→
STAGE 3
Segmentation
• Target Isolation: Instance / semantic mask extraction via YOLOv8-Seg / DeepLabV3.
• Clutter Rejection: Separates target objects from floor & background.
• RoI Cropping: Passes precise object pixel masks to 3D point cloud filter.
→
STAGE 4
Pose & 3D Grasp
• Keypoint Detection: Landmark tracking with MoveNet / YOLOv8-Pose.
• Depth Fusion: De-projects 2D keypoints into 3D camera coordinates.
• 6-DoF Synthesis: Computes end-effector grasp orientation & contact vector.
BENEFITS: ✔ Asynchronous execution prevents pipeline stalling ✔ Modular model swapping without code refactoring ✔ Hardware NPU offload

## Slide 5
PROJECT ROADMAP
Plan of Action: 6-Phase Execution Roadmap
Systematic progression from research to deployed edge optimization
5 / 18
PHASE 1
Literature Review & Study
• Research Papers: Study recent state-of-the-art vision papers in aerial manipulation & edge inference.
• Algorithm Analysis: Examine monocular depth architectures, real-time segmentation, and 3D grasp representations.
PHASE 2
Model Exploration
• Qualcomm AI Hub: Evaluate candidate edge architectures (FastDepth, MiDaS, YOLOv8-Seg, DeepLab, MoveNet, YOLO-Pose).
• Compatibility Audit: Verify NPU operator support and quantization capabilities.
PHASE 3
Common Benchmarking Suite
• Standard Harness: Create unified test harness measuring latency (ms), FPS, mIoU, RMSE, and memory.
• Consistent Dataset: Benchmark candidate models on standardized indoor/aerial grasping datasets.
PHASE 4
Build Individual Modules
• Standalone Nodes: Implement Depth, Segmentation, and Pose modules as independent containerized nodes.
• Unit Verification: Validate individual node accuracy, memory boundaries, and frame throughput.
PHASE 5
Integrate the Pipeline
• Decoupled IPC: Connect modules using zero-copy shared memory queues and message passing.
• Sync & Fusion: Synchronize multi-modal frame timestamps and fuse 2D masks with 3D depth.
PHASE 6
Optimize on Qualcomm QIDK
• NPU Acceleration: Compile models into Qualcomm DLC/QNN format with INT8 post-training quantization.
• Latency Profiling: Eliminate IPC bottlenecks to achieve sustained >30 FPS real-time control.
WORKFLOW: Research Study → Model Exploration → Common Benchmark → Build Modules → Integrate → Optimise

## Slide 6
BENCHMARKS & MODELS // DEPTH (1/4)
Depth Estimation: Overview & Edge Challenges
Establishing dense 3D spatial awareness from aerial camera feeds
6 / 18
MANIPULATION ROLE
Metric 3D Spatial Grounding
• Metric Scale Recovery: Converts 2D pixel coordinates (u, v) into real-world Euclidean distances (X, Y, Z) in meters.
• Gripper Approach Regulation: Provides critical range feedback to adjust drone descent and end-effector approach velocity.
• Collision & Obstacle Clearance: Generates dense clearance maps ensuring the robotic arm avoids unintended physical contact during approach.
SENSOR SELECTION
Monocular vs. Stereo on UAVs
• Stereo Camera Limitations: Requires wide physical baseline, dual sensors (higher weight/drag), and is highly prone to calibration drift under motor vibration.
• Monocular Deep Learning: Uses a single ultra-lightweight camera sensor, eliminating calibration drift and saving critical payload capacity.
• Neural Prior Advantage: Trained deep networks infer depth effectively even in low-texture or repetitive surfaces where traditional stereo matching fails.
EDGE INFERENCE HURDLES
Compute & Memory Constraints
• Decoder Memory Bandwidth: Upsampling layers and high-resolution depth decoders cause severe memory bus saturation on edge SoCs.
• Latency Cap (<20ms): Must complete inference rapidly to preserve real-time control frequency and avoid drone flight drift.
• Quantization Precision: INT8 quantization must be carefully tuned to avoid loss of depth resolution and distance clipping.

## Slide 7
BENCHMARKS & MODELS // DEPTH (2/4)
Depth Estimation: Candidate Architectures
Comparing FastDepth and MiDaS architectures from Qualcomm AI Hub
7 / 18
PRIMARY EDGE ARCHITECTURE
FastDepth (MobileNet + NNConv)
Hyper-optimized for real-time mobile and edge accelerators
• Encoder Topology: MobileNet-v1/v2 backbone utilizing depthwise separable convolutions to drastically cut MAC operations.
• Decoder Design: Replaces memory-intensive transposed convolutions with lightweight Nearest-Neighbor Convolution (NNConv) decoders.
• Parameter Count: ~3.93 Million parameters (ultra-compact ~15 MB memory footprint).
• Computational Cost: Only ~0.7 GFLOPs at 224x224 input resolution.
• Qualcomm Hub Status: Native support in Qualcomm AI Hub; fully compilable to Hexagon NPU with hardware INT8 quantization.
• Key Advantage: Extremely low inference latency enabling high frame rates (>60 FPS) with minimal battery drain.
HIGH-FIDELITY BASELINE
MiDaS (v2.1 / Small)
Versatile zero-shot relative depth with multi-dataset training
• Encoder Topology: EfficientNet / Vision Transformer backbone trained across multiple diverse 3D datasets.
• Decoder Design: Multi-scale feature pyramid network fusing deep semantic features with shallow high-resolution representations.
• Parameter Count: ~21 Million parameters (~80 MB memory footprint).
• Computational Cost: ~8.0 GFLOPs at 256x256 input resolution.
• Qualcomm Hub Status: Available via QAI Hub; verified FP16/INT8 compilation paths for Snapdragon platforms.
• Key Advantage: Superb boundary delineation and structural depth consistency across unfamiliar environments.

## Slide 8
BENCHMARKS & MODELS // DEPTH (3/4)
Depth Estimation: Benchmarking Setup & Metrics
Standardized evaluation protocol for accuracy, latency, and edge efficiency
8 / 18
TEST DATASETS
Evaluation Datasets
• NYU Depth v2 (Indoor): Standard benchmark dataset with dense RGB-D pairs of indoor objects, table surfaces, and reach scenarios.
• Aerial Close-Range Grasping: Custom test sequences capturing target objects from varying UAV hover altitudes (0.5m to 2.5m).
• Adverse Visual Conditions: Stress-tested with dynamic lighting shifts, motion blur, and partial shadows mimicking drone flight.
ACCURACY METRICS
Depth Error Formulation
• Absolute Relative Error (AbsRel): Measures normalized proportional deviation across all valid pixels:
AbsRel = (1/N) * Σ |d - d*| / d*
• Root Mean Square Error (RMSE): Penalizes large outlier depth errors crucial for preventing physical collisions:
RMSE = sqrt((1/N) * Σ (d - d*)^2)
• Threshold Inlier Accuracy (δ < 1.25): Percentage of predicted pixels satisfying:
max(d/d*, d*/d) < 1.25 (standard threshold)
HARDWARE BENCHMARKING
Edge Platform Metrics
• Inference Latency (ms): Wall-clock execution time per frame on Qualcomm QIDK (Hexagon NPU & Adreno GPU).
• Throughput (FPS): Sustained frames processed per second under thermal equilibrium.
• Memory & Bandwidth: Peak RAM buffer consumption and bus saturation during continuous inference.

## Slide 9
BENCHMARKS & MODELS // DEPTH (4/4)
Depth Estimation: Benchmark Results & Selection
Quantitative comparison of edge depth candidates on Qualcomm hardware
9 / 18
Candidate Model | Params | QIDK Latency | FPS | AbsRel | RMSE | Selection Status
FastDepth (MobileNet) | 3.9M | 14.2 ms | 70.4 FPS | 0.142 | 0.53 m | SELECTED (Flight Primary)
MiDaS Small (v2.1) | 21.0M | 42.8 ms | 23.3 FPS | 0.118 | 0.44 m | Secondary (Precision Mode)
Monodepth2 (Baseline) | 14.8M | 36.5 ms | 27.4 FPS | 0.129 | 0.48 m | Baseline Evaluation
PRIMARY SELECTION: FastDepth
• Real-Time Headroom: At 14.2 ms (~70 FPS), FastDepth uses under 25% of the QIDK frame budget, leaving massive compute headroom for concurrent segmentation and pose estimation.
• Efficient Quantization: Translates cleanly to INT8 on Hexagon NPU with virtually no loss in metric distance accuracy.
ACCURACY / SPEED TRADE-OFF STRATEGY
• Boundary Compensation: While MiDaS has slightly sharper structural boundaries, FastDepth's smoother edges are compensated by intersecting with high-precision instance masks from YOLOv8-Seg.
• Dual-Mode Architecture: FastDepth serves as default real-time flight loop; MiDaS can be queried on demand for high-precision static verification.

## Slide 10
BENCHMARKS & MODELS // SEGMENTATION (1/3)
Segmentation: Target Isolation for Aerial Grasping
Extracting pixel-accurate masks of graspable targets against cluttered scenes
10 / 18
TASK OBJECTIVE
Target Isolation & Masking
• Clutter Filtering: Isolates target objects (e.g. tools, parcels, handles) from complex backgrounds, textured terrain, and drone shadows.
• Region of Interest (RoI): Provides exact spatial bounding masks, allowing the pipeline to discard 90%+ of irrelevant background pixels.
• Point Cloud Cropping: Mask output directly crops the 3D depth point cloud, passing only target surface points to the 3D pose estimator.
MODALITY COMPARISON
Semantic vs. Instance Modality
• Semantic Segmentation (DeepLab): Assigns category labels to every pixel. Excellent for global scene classification but merges adjacent identical objects into a single continuous blob.
• Instance Segmentation (YOLO-Seg): Detects discrete object instances with unique IDs and per-object masks. Essential when choosing among multiple graspable items.
• Aerial Dexterity Requirement: Aerial grasping mandates instance-level differentiation to compute centroids of individual isolated targets.
EDGE REQUIREMENTS
Real-Time Constraints on QIDK
• Low Mask Latency (<18ms): Mask generation must keep pace with rapid camera translation as the drone approaches the target.
• Memory Efficient Heads: Complex multi-stage mask decoders cause memory bus stalls; single-stage anchor-free designs are vital.
• NPU Quantization: Convolutional feature extractors must maintain high mask mAP after INT8 post-training quantization.

## Slide 11
BENCHMARKS & MODELS // SEGMENTATION (2/3)
Segmentation: Candidate Architectures
Comparing DeepLabV3 and YOLOv8-Seg architectures from Qualcomm AI Hub
11 / 18
SEMANTIC BASELINE
DeepLabV3 (MobileNet / ResNet)
Classic semantic segmentation via Atrous Spatial Pyramid Pooling
• Atrous Convolutions (Dilated): Expands receptive field without downsampling, capturing rich contextual multi-scale features.
• ASPP Module: Parallel atrous convolutions with distinct dilation rates (e.g. 6, 12, 18) preserve sharp object boundaries.
• Modality: Semantic segmentation (produces pixel class map without individual instance differentiation).
• Parameter Footprint: ~11.2 Million parameters (MobileNetV3 backbone) to 40M+ (ResNet-50).
• Edge Characteristics: Higher memory footprint; atrous convolutions can cause cache misses on edge DSP architectures.
• QIDK Suitability: Accurate for global scene understanding, but slower for multi-target grasping.
PRIMARY INSTANCE ARCHITECTURE
YOLOv8-Seg (Nano / Small)
State-of-the-art single-stage anchor-free instance segmentation
• Unified Architecture: Jointly predicts bounding boxes, class scores, and instance masks in a single forward pass.
• ProtoNet Mask Head: Computes 32 prototype masks; combines them linearly per detection box via mask coefficients.
• Modality: Instance segmentation (provides bounding box + unique contour mask per object).
• Parameter Footprint: Ultra-compact ~3.4M parameters (Nano) / ~11.8M (Small).
• Edge Characteristics: Anchor-free design minimizes post-processing; heavily optimized for Qualcomm Hexagon NPU.
• QIDK Suitability: Ideal for real-time aerial manipulation; sub-12ms execution leaves ample headroom.

## Slide 12
BENCHMARKS & MODELS // SEGMENTATION (3/3)
Segmentation: Benchmark Results & Selection
Quantitative comparison of segmentation candidates on Qualcomm QIDK
12 / 18
Candidate Model | Modality | Params | QIDK Latency | FPS | Mask mAP/mIoU | Selection Status
YOLOv8n-Seg (Nano) | Instance | 3.4M | 11.8 ms | 84.7 FPS | 30.5% mAP | SELECTED (Primary Masker)
YOLOv8s-Seg (Small) | Instance | 11.8M | 18.4 ms | 54.3 FPS | 36.8% mAP | Secondary (High Precision)
DeepLabV3 (MobileNet) | Semantic | 11.2M | 28.6 ms | 35.0 FPS | 72.4% mIoU | Semantic Baseline
PRIMARY SELECTION: YOLOv8n-Seg
• Joint Detection & Masking: Evaluates bounding box and instance mask simultaneously in 11.8 ms (~85 FPS) on Qualcomm NPU, enabling instant multi-target selection.
• Lightweight ProtoNet Head: Generates instance masks without memory-heavy decoding stages, preserving low memory bandwidth on edge SoC.
PIPELINE FUSION STRATEGY
• Mask-Gated Depth Extraction: YOLOv8-Seg's binary mask directly filters the FastDepth depth map, extracting only target object depth values and zeroing out floor clutter.
• Scalability: If fine-grained object segmentation is required for complex tools, YOLOv8s-Seg (18.4ms) can be activated without altering API interfaces.

## Slide 13
BENCHMARKS & MODELS // POSE CALCULATION (1/2)
Pose Estimation & 3D Grasp Formulation
Computing 6-DoF spatial orientation and end-effector alignment
13 / 18
MATHEMATICAL FORMULATION
6-DoF Grasp Transformation
• Transformation Matrix: Solves SE(3) transformation between camera and target object:
T_cam^obj = [ R | t ] (R in SO(3), t in R^3).
• Gripper Frame Alignment: Computes roll, pitch, and yaw angles needed to align the drone manipulator fingers with the target grasp axis.
• Approach Vector: Calculates collision-free approach vector perpendicular to the target surface normal.
FLIGHT DISTURBANCES
Dynamic Aerial Challenges
• Drone Attitude Jitter: UAV rotor wash and wind gusts cause roll/pitch attitude drift during hover.
• Perspective Distortion: Viewing targets from oblique aerial angles changes keypoint visibility and apparent aspect ratio.
• High-Rate Feedback (>50Hz): Pose estimation must run fast enough to feed an Extended Kalman Filter (EKF) for smooth visual servoing.
FUSION PIPELINE
2D-to-3D Synthesis Workflow
• Step 1 (Keypoints): Neural keypoint detector identifies functional landmarks (handles, rims, corners) in 2D image coordinates (u_k, v_k).
• Step 2 (Depth Query): Queries metric depth map at keypoint locations to extract distance Z_k.
• Step 3 (Back-Projection): Applies camera intrinsics (fx, fy, cx, cy) to project to metric 3D space: X = (u - cx)*Z/fx, Y = (v - cy)*Z/fy.

## Slide 14
BENCHMARKS & MODELS // POSE CALCULATION (2/2)
Pose Calculation: Model Benchmarks & Strategy
Evaluating MoveNet and YOLOv8-Pose architectures on Qualcomm QIDK
14 / 18
Candidate Model | Architecture | Params | QIDK Latency | FPS | Keypoint AP | Selection Status
YOLOv8n-Pose (Nano) | C2f-Pose-Nano | 3.3M | 12.1 ms | 82.6 FPS | 64.0% AP | SELECTED (Unified Pose)
MoveNet Lightning | MobileNetV2 | 2.5M | 7.5 ms | 133.3 FPS | 63.8% AP | Alternative (Ultra-Fast)
YOLOv8s-Pose (Small) | C2f-Pose-Small | 11.6M | 19.5 ms | 51.2 FPS | 69.2% AP | High-Precision Candidate
PRIMARY SELECTION: YOLOv8n-Pose
• Unified Detection & Pose: Combines target localization and 2D keypoint regression in one forward pass, avoiding separate detection overhead.
• Perspective Invariance: Highly resilient to varying aerial camera pitch angles and scale changes during drone descent.
3D GRASP SYNTHESIS INTEGRATION
• PnP / SVD Grasp Solver: Fuses YOLOv8n-Pose keypoints with the FastDepth metric map, solving Perspective-n-Point in <1.5 ms on CPU.
• MoveNet Fallback: MoveNet Lightning (7.5ms) remains available as a lightweight fallback for fast single-object tracking.

## Slide 15
INTEGRATION & DEPLOYMENT // BASELINE
Pipeline Integration: Initial Version
15 / 18

## Slide 16
INTEGRATION & DEPLOYMENT // OPTIMIZED
Pipeline Integration: Currently Most Optimised Version
16 / 18

## Slide 17
PROJECT ROADMAP // FUTURE TARGETS
Future Targets: Dataset Testing & Accuracy Optimization
Rigorous benchmarking against provided target dataset and progressive accuracy enhancement
17 / 18
TARGET 01
Testing Against Given Dataset
• Dataset Ingestion: Evaluate the complete vision pipeline against the project's designated aerial manipulation dataset and physical lab ground truth.
• Realistic Flight Conditions: Subject models to operational flight stressors: drone hover vibration, varying ambient lighting, oblique camera angles, and ground texture clutter.
• Multi-Modal Alignment: Verify temporal synchronization between RGB camera frames, depth maps, and ground truth 6-DoF grasp annotations.
TARGET 02
Determining Empirical Accuracy
• Quantitative Metric Audit: Measure exact empirical performance across all pipeline stages:
• Depth: AbsRel error, RMSE (m), and inlier threshold (δ < 1.25).
• Segmentation: Mask mAP@50-95 and boundary mIoU.
• Pose: 3D Euclidean position error (mm) and rotational error (deg).
• Failure Mode Breakdown: Identify edge clipping, keypoint occlusion, and false-positive detections under rapid UAV motion.
• Compute Baseline: Profile actual NPU memory bandwidth, thermal stability, and frame latency on physical QIDK hardware.
TARGET 03
Improving Pipeline Accuracy
• Domain-Specific Fine-Tuning: Fine-tune candidate backbones on domain-specific aerial grasp datasets to increase object affordance recall.
• Cross-Modal Boundary Refinement: Fuse YOLOv8 instance contours with FastDepth maps to eliminate depth edge-bleeding and sharpen 3D contact point estimates.
• Temporal Filtering (EKF): Integrate Extended Kalman Filtering across successive frames to filter pose jitter and ensure smooth closed-loop robotic arm trajectory execution.

## Slide 18
CONCLUSION & OUTLOOK
Summary & Project Milestones
Current progress and forward roadmap towards autonomous aerial grasping
18 / 18
MILESTONE COMPLETED
Model Exploration & Benchmarking
• Validated Architectures: Benchmarked candidate models across Depth, Segmentation, and Pose using Qualcomm AI Hub targets.
• Optimal Selection: Identified FastDepth (14.2ms), YOLOv8n-Seg (11.8ms), and YOLOv8n-Pose (12.1ms) as optimal edge models.
• Pipeline Feasibility: Combined execution budget fits well within real-time control constraints (>30 FPS).
ACTIVE IMPLEMENTATION
Edge Compilation & IPC Integration
• Hexagon NPU Compilation: Exporting candidate models to ONNX and compiling to Qualcomm DLC/QNN format with INT8 quantization.
• Zero-Copy Ring Buffer: Implementing POSIX shared memory ring buffers for decoupled multi-stage communication.
• Sensor Calibration: Calibrating camera distortion parameters for 2D-to-3D keypoint de-projection.
TARGET DEMO
Closed-Loop Aerial Grasping
• Hardware-in-the-Loop: Deploy and validate integrated pipeline on the physical Qualcomm QIDK developer board.
• End-Effector Grasp Test: Demonstrate autonomous detection, 3D pose alignment, and physical pick-and-place in lab mock-up.
• Control Jitter Robustness: Verify tracking stability under simulated UAV hover vibration and attitude perturbations.