## Slide 1
EMBEDDED SYSTEMS WORKSHOP
Aerial Manipulation
AI-Enabled Perception & 3D Grasping Pipeline on the Qualcomm QIDK Platform
PROJECT MEMBERS
S.L.A. Kartikeya • N.L. Sankeerth • Pranathi Giri • Yashitha Chennupati
Prof: Spandan Roy | Mentor: Sarthak Mishra | TA: Aryama Murthy

## Slide 2
PROJECT OVERVIEW
Problem Statement
Optimizing multi-task robotic vision under strict aerial edge constraints
2 / 18
CORE OBJECTIVE
Build an optimized, real-time software pipeline integrating depth analysis, segmentation, 3D grasping, and pose calculation onboard the Qualcomm QIDK platform.
01 • SWaP & EDGE COMPUTE
Severe Aerial Resource Limits
• Strict Power Envelope: UAV battery limitations mandate ultra-low wattage compute (<15W) with zero thermal throttling.
• Fully Onboard Autonomy: Must process raw camera feeds on Qualcomm QIDK without ground-station offload dependencies.
• Memory Bandwidth Limits: Concurrent deep neural networks compete for shared edge SoC memory bus.
02 • LATENCY BOTTLENECK
Multi-Task Vision Lag
• Cumulative Delays: Running Depth, Segmentation, and Pose sequentially accumulates frame lags (>150ms), destabilizing flight control.
• Throughput Requirement: Grasping moving/hovering targets requires deterministic real-time processing (>30 FPS).
• Heterogeneous Scheduling: Demands balanced pipelining across Kryo CPU, Adreno GPU, and Hexagon NPU.
03 • AERIAL DYNAMICS
Dynamic Flight Perturbations
• Hover Jitter & Vibration: Rotor oscillations and aerodynamic wash introduce high visual blur and camera parallax.
• Spatial Grasp Precision: Requires millimeter-level 3D grasp coordinates despite target and drone movement.
• Continuous Re-planning: Pose estimates must update dynamically as the robotic end-effector nears contact.

## Slide 3
CONTEXT & SIGNIFICANCE
Project Motivation
Transforming UAVs from passive observers to interactive physical agents
3 / 18
PARADIGM SHIFT
From Passive Sensing to Physical Interaction
• Beyond Observation: Conventional drones are strictly limited to inspection and photography. Aerial manipulation empowers drones to physically interact with their environment.
• High-Impact Applications: Enables remote valve turning in refineries, hazardous waste retrieval, search-and-rescue payload delivery, and structural repair.
• Complex Manipulator Mechanics: Requires closed-loop coordination between aerial flight dynamics and lightweight multi-DoF robotic arms.
AUTONOMY REQUIREMENT
Necessity of Zero-Lag Onboard Intelligence
• Fragility of Teleoperation: RF links in industrial or disaster zones suffer from signal shadowing, high packet jitter, and total dropouts.
• Safety-Critical Dynamics: Physical contact with objects exerts reaction forces on the drone. A 100ms latency spike can cause immediate flight instability or crashes.
• Closed-Loop Control: Perception must run at camera frame rate (>30 FPS) to feed visual servoing algorithms without lag.
HARDWARE ENABLER
The Qualcomm QIDK Platform Advantage
• Heterogeneous Compute: Combines high-performance Qualcomm Kryo CPU, Adreno GPU, and Hexagon NPU with dedicated vector/tensor accelerators.
• Qualcomm AI Hub: Provides pre-compiled, optimized neural backbones with hardware-specific INT8/FP16 quantization.
• Optimal Energy Efficiency: Achieves peak deep learning TOPS per watt, preserving flight battery longevity and payload flight endurance.

## Slide 4
SYSTEM ARCHITECTURE
Proposed Solution: Modular Vision Pipeline
Decoupled multi-stage architecture with independent execution nodes
4 / 18
ARCHITECTURAL PRINCIPLE: Complete decoupling of all stages communicating via zero-copy inter-process communication.
STAGE 1
Image Capture
• Camera Interface: MIPI-CSI / USB3 camera driver at 60 FPS.
• Pre-processing: Hardware ISP debayering, undistortion & rectification.
• Buffer Dispatch: Feeds shared memory ring buffer for parallel consumer nodes.
→
STAGE 2
Depth Calculation
• Neural Monocular: Real-time depth estimation using FastDepth / MiDaS.
• Metric Scaling: Computes dense distance maps for metric Z coordinates.
• Obstacle Map: Assists collision clearance during manipulator approach.
→
STAGE 3
Segmentation
• Target Isolation: Instance / semantic mask extraction via YOLOv8-Seg / DeepLabV3.
• Clutter Rejection: Separates target objects from floor & background.
• RoI Cropping: Passes precise object pixel masks to 3D point cloud filter.
→
STAGE 4
Pose & 3D Grasp
• Keypoint Detection: Landmark tracking with MoveNet / YOLOv8-Pose.
• Depth Fusion: De-projects 2D keypoints into 3D camera coordinates.
• 6-DoF Synthesis: Computes end-effector grasp orientation & contact vector.
BENEFITS: ✔ Asynchronous execution prevents pipeline stalling ✔ Modular model swapping without code refactoring ✔ Hardware NPU offload

## Slide 5
PROJECT ROADMAP
Plan of Action: 6-Phase Execution Roadmap
Systematic progression from research to deployed edge optimization
5 / 18
PHASE 1
Literature Review & Study
• Research Papers: Study recent state-of-the-art vision papers in aerial manipulation & edge inference.
• Algorithm Analysis: Examine monocular depth architectures, real-time segmentation, and 3D grasp representations.
PHASE 2
Model Exploration
• Qualcomm AI Hub: Evaluate candidate edge architectures (FastDepth, MiDaS, YOLOv8-Seg, DeepLab, MoveNet, YOLO-Pose).
• Compatibility Audit: Verify NPU operator support and quantization capabilities.
PHASE 3
Common Benchmarking Suite
• Standard Harness: Create unified test harness measuring latency (ms), FPS, mIoU, RMSE, and memory.
• Consistent Dataset: Benchmark candidate models on standardized indoor/aerial grasping datasets.
PHASE 4
Build Individual Modules
• Standalone Nodes: Implement Depth, Segmentation, and Pose modules as independent containerized nodes.
• Unit Verification: Validate individual node accuracy, memory boundaries, and frame throughput.
PHASE 5
Integrate the Pipeline
• Decoupled IPC: Connect modules using zero-copy shared memory queues and message passing.
• Sync & Fusion: Synchronize multi-modal frame timestamps and fuse 2D masks with 3D depth.
PHASE 6
Optimize on Qualcomm QIDK
• NPU Acceleration: Compile models into Qualcomm DLC/QNN format with INT8 post-training quantization.
• Latency Profiling: Eliminate IPC bottlenecks to achieve sustained >30 FPS real-time control.
WORKFLOW: Research Study → Model Exploration → Common Benchmark → Build Modules → Integrate → Optimise

## Slide 6
BENCHMARKS & MODELS // DEPTH (1/4)
Depth Estimation: Overview & Edge Challenges
Establishing dense 3D spatial awareness from aerial camera feeds
6 / 18
MANIPULATION ROLE
Metric 3D Spatial Grounding
• Metric Scale Recovery: Converts 2D pixel coordinates (u, v) into real-world Euclidean distances (X, Y, Z) in meters.
• Gripper Approach Regulation: Provides critical range feedback to adjust drone descent and end-effector approach velocity.
• Collision & Obstacle Clearance: Generates dense clearance maps ensuring the robotic arm avoids unintended physical contact during approach.
SENSOR SELECTION
Monocular vs. Stereo on UAVs
• Stereo Camera Limitations: Requires wide physical baseline, dual sensors (higher weight/drag), and is highly prone to calibration drift under motor vibration.
• Monocular Deep Learning: Uses a single ultra-lightweight camera sensor, eliminating calibration drift and saving critical payload capacity.
• Neural Prior Advantage: Trained deep networks infer depth effectively even in low-texture or repetitive surfaces where traditional stereo matching fails.
EDGE INFERENCE HURDLES
Compute & Memory Constraints
• Decoder Memory Bandwidth: Upsampling layers and high-resolution depth decoders cause severe memory bus saturation on edge SoCs.
• Latency Cap (<20ms): Must complete inference rapidly to preserve real-time control frequency and avoid drone flight drift.
• Quantization Precision: INT8 quantization must be carefully tuned to avoid loss of depth resolution and distance clipping.

## Slide 7
BENCHMARKS & MODELS // DEPTH (2/4)
Depth Estimation: Candidate Architectures
Comparing FastDepth and MiDaS architectures from Qualcomm AI Hub
7 / 18
PRIMARY EDGE ARCHITECTURE
FastDepth (MobileNet + NNConv)
Hyper-optimized for real-time mobile and edge accelerators
• Encoder Topology: MobileNet-v1/v2 backbone utilizing depthwise separable convolutions to drastically cut MAC operations.
• Decoder Design: Replaces memory-intensive transposed convolutions with lightweight Nearest-Neighbor Convolution (NNConv) decoders.
• Parameter Count: ~3.93 Million parameters (ultra-compact ~15 MB memory footprint).
• Computational Cost: Only ~0.7 GFLOPs at 224x224 input resolution.
• Qualcomm Hub Status: Native support in Qualcomm AI Hub; fully compilable to Hexagon NPU with hardware INT8 quantization.
• Key Advantage: Extremely low inference latency enabling high frame rates (>60 FPS) with minimal battery drain.
HIGH-FIDELITY BASELINE
MiDaS (v2.1 / Small)
Versatile zero-shot relative depth with multi-dataset training
• Encoder Topology: EfficientNet / Vision Transformer backbone trained across multiple diverse 3D datasets.
• Decoder Design: Multi-scale feature pyramid network fusing deep semantic features with shallow high-resolution representations.
• Parameter Count: ~21 Million parameters (~80 MB memory footprint).
• Computational Cost: ~8.0 GFLOPs at 256x256 input resolution.
• Qualcomm Hub Status: Available via QAI Hub; verified FP16/INT8 compilation paths for Snapdragon platforms.
• Key Advantage: Superb boundary delineation and structural depth consistency across unfamiliar environments.

## Slide 8
BENCHMARKS & MODELS // DEPTH (3/4)
Depth Estimation: Benchmarking Setup & Metrics
Standardized evaluation protocol for accuracy, latency, and edge efficiency
8 / 18
TEST DATASETS
Evaluation Datasets
• NYU Depth v2 (Indoor): Standard benchmark dataset with dense RGB-D pairs of indoor objects, table surfaces, and reach scenarios.
• Aerial Close-Range Grasping: Custom test sequences capturing target objects from varying UAV hover altitudes (0.5m to 2.5m).
• Adverse Visual Conditions: Stress-tested with dynamic lighting shifts, motion blur, and partial shadows mimicking drone flight.
ACCURACY METRICS
Depth Error Formulation
• Absolute Relative Error (AbsRel): Measures normalized proportional deviation across all valid pixels:
AbsRel = (1/N) * Σ |d - d*| / d*
• Root Mean Square Error (RMSE): Penalizes large outlier depth errors crucial for preventing physical collisions:
RMSE = sqrt((1/N) * Σ (d - d*)^2)
• Threshold Inlier Accuracy (δ < 1.25): Percentage of predicted pixels satisfying:
max(d/d*, d*/d) < 1.25 (standard threshold)
HARDWARE BENCHMARKING
Edge Platform Metrics
• Inference Latency (ms): Wall-clock execution time per frame on Qualcomm QIDK (Hexagon NPU & Adreno GPU).
• Throughput (FPS): Sustained frames processed per second under thermal equilibrium.
• Memory & Bandwidth: Peak RAM buffer consumption and bus saturation during continuous inference.

## Slide 9
BENCHMARKS & MODELS // DEPTH (4/4)
Depth Estimation: Benchmark Results & Selection
Quantitative comparison of edge depth candidates on Qualcomm hardware
9 / 18
Model (input, precision) | Params | QIDK NPU Latency | NPU Throughput | AbsRel* | RMSE* | Selection Status
DA-V2 Small @280, INT8 | 24.2M | 3.3 ms | 309 inf/s | 0.081 | 0.36 m | FPS Mode (60 fps)
DA-V2 Small @392, INT8 | 24.2M | 6.0 ms | 168 inf/s | 0.071 | 0.33 m | SELECTED (Balance)
DA-V2 Small @518, INT8 | 24.2M | 12.9 ms | 74 inf/s | — | — | Quality Mode
PRIMARY SELECTION: Depth Anything V2 Small
• Why it replaced FastDepth/MiDaS: ViT-S encoder gives sharper object boundaries and robust zero-shot depth; 24.2M params fits the Hexagon HTP after INT8 quantization.
• Measured on QIDK SM8650: 6.0 ms pure NPU time at 392² (snpe-net-run, 100 runs, burst), 14x smaller DLC than the ViT-L model we started with (682 MB → 50 MB).
ACCURACY / SPEED TRADE-OFF STRATEGY
• Three resolutions, one model: 280² / 392² / 518² trade 3.3 → 12.9 ms NPU time for finer depth detail; chosen per app variant without code changes.
• *Accuracy protocol: NYU Depth v2 test (654 imgs), float reference, scale-shift aligned in disparity (relative-depth model), Eigen crop. '—' = evaluation in progress.

## Slide 10
BENCHMARKS & MODELS // SEGMENTATION (1/3)
Segmentation: Target Isolation for Aerial Grasping
Extracting pixel-accurate masks of graspable targets against cluttered scenes
10 / 18
TASK OBJECTIVE
Target Isolation & Masking
• Clutter Filtering: Isolates target objects (e.g. tools, parcels, handles) from complex backgrounds, textured terrain, and drone shadows.
• Region of Interest (RoI): Provides exact spatial bounding masks, allowing the pipeline to discard 90%+ of irrelevant background pixels.
• Point Cloud Cropping: Mask output directly crops the 3D depth point cloud, passing only target surface points to the 3D pose estimator.
MODALITY COMPARISON
Semantic vs. Instance Modality
• Semantic Segmentation (DeepLab): Assigns category labels to every pixel. Excellent for global scene classification but merges adjacent identical objects into a single continuous blob.
• Instance Segmentation (YOLO-Seg): Detects discrete object instances with unique IDs and per-object masks. Essential when choosing among multiple graspable items.
• Aerial Dexterity Requirement: Aerial grasping mandates instance-level differentiation to compute centroids of individual isolated targets.
EDGE REQUIREMENTS
Real-Time Constraints on QIDK
• Low Mask Latency (<18ms): Mask generation must keep pace with rapid camera translation as the drone approaches the target.
• Memory Efficient Heads: Complex multi-stage mask decoders cause memory bus stalls; single-stage anchor-free designs are vital.
• NPU Quantization: Convolutional feature extractors must maintain high mask mAP after INT8 post-training quantization.

## Slide 11
BENCHMARKS & MODELS // SEGMENTATION (2/3)
Segmentation: Candidate Architectures
Comparing DeepLabV3 and YOLOv8-Seg architectures from Qualcomm AI Hub
11 / 18
SEMANTIC BASELINE
DeepLabV3 (MobileNet / ResNet)
Classic semantic segmentation via Atrous Spatial Pyramid Pooling
• Atrous Convolutions (Dilated): Expands receptive field without downsampling, capturing rich contextual multi-scale features.
• ASPP Module: Parallel atrous convolutions with distinct dilation rates (e.g. 6, 12, 18) preserve sharp object boundaries.
• Modality: Semantic segmentation (produces pixel class map without individual instance differentiation).
• Parameter Footprint: ~11.2 Million parameters (MobileNetV3 backbone) to 40M+ (ResNet-50).
• Edge Characteristics: Higher memory footprint; atrous convolutions can cause cache misses on edge DSP architectures.
• QIDK Suitability: Accurate for global scene understanding, but slower for multi-target grasping.
PRIMARY INSTANCE ARCHITECTURE
YOLOv8-Seg (Nano / Small)
State-of-the-art single-stage anchor-free instance segmentation
• Unified Architecture: Jointly predicts bounding boxes, class scores, and instance masks in a single forward pass.
• ProtoNet Mask Head: Computes 32 prototype masks; combines them linearly per detection box via mask coefficients.
• Modality: Instance segmentation (provides bounding box + unique contour mask per object).
• Parameter Footprint: Ultra-compact ~3.4M parameters (Nano) / ~11.8M (Small).
• Edge Characteristics: Anchor-free design minimizes post-processing; heavily optimized for Qualcomm Hexagon NPU.
• QIDK Suitability: Ideal for real-time aerial manipulation; sub-12ms execution leaves ample headroom.

## Slide 12
BENCHMARKS & MODELS // SEGMENTATION (3/3)
Segmentation: Benchmark Results & Selection
Quantitative comparison of segmentation candidates on Qualcomm QIDK
12 / 18
Model (input) | Precision | Params | QIDK NPU Latency | NPU Throughput | Mask mAP* | Selection Status
YOLOv8n-Seg @384 | W8A8 | 3.4M | 0.5 ms | 1599 inf/s | — | FPS Mode (60 fps)
YOLOv8n-Seg @640 | W8A8 | 3.4M | 1.1 ms | 643 inf/s | 30.5% | SELECTED (Balance)
YOLOv8n-Seg @640 | W8A16 | 3.4M | 2.8 ms | 288 inf/s | 30.5% | Quality Mode
PRIMARY SELECTION: YOLOv8n-Seg (decoupled head)
• Measured on QIDK SM8650: 1.1 ms pure NPU time at 640² INT8; boxes, scores, mask coefficients and prototypes exported as separate outputs so each gets its own quantization scale.
• Replaced YOLOv8x-Seg: 143 MB YOLOv8x-Seg caused DSP out-of-memory when running alongside depth; YOLOv8n-Seg DLC is 8 MB.
PIPELINE FUSION STRATEGY
• Mask-Gated Depth: Instance masks select the target's depth pixels; background and floor are discarded before 3D back-projection.
• *mAP: COCO val2017 mask mAP50-95 of the float model at 640 (Ultralytics reference); INT8 on-device evaluation in progress.

## Slide 13
BENCHMARKS & MODELS // POSE CALCULATION (1/2)
Pose Estimation & 3D Grasp Formulation
Computing 6-DoF spatial orientation and end-effector alignment
13 / 18
MATHEMATICAL FORMULATION
6-DoF Grasp Transformation
• Transformation Matrix: Solves SE(3) transformation between camera and target object:
T_cam^obj = [ R | t ] (R in SO(3), t in R^3).
• Gripper Frame Alignment: Computes roll, pitch, and yaw angles needed to align the drone manipulator fingers with the target grasp axis.
• Approach Vector: Calculates collision-free approach vector perpendicular to the target surface normal.
FLIGHT DISTURBANCES
Dynamic Aerial Challenges
• Drone Attitude Jitter: UAV rotor wash and wind gusts cause roll/pitch attitude drift during hover.
• Perspective Distortion: Viewing targets from oblique aerial angles changes keypoint visibility and apparent aspect ratio.
• High-Rate Feedback (>50Hz): Pose estimation must run fast enough to feed an Extended Kalman Filter (EKF) for smooth visual servoing.
FUSION PIPELINE
2D-to-3D Synthesis Workflow
• Step 1 (Keypoints): Neural keypoint detector identifies functional landmarks (handles, rims, corners) in 2D image coordinates (u_k, v_k).
• Step 2 (Depth Query): Queries metric depth map at keypoint locations to extract distance Z_k.
• Step 3 (Back-Projection): Applies camera intrinsics (fx, fy, cx, cy) to project to metric 3D space: X = (u - cx)*Z/fx, Y = (v - cy)*Z/fy.

## Slide 14
BENCHMARKS & MODELS // POSE CALCULATION (2/2)
Pose Calculation: Model Benchmarks & Strategy
Evaluating MoveNet and YOLOv8-Pose architectures on Qualcomm QIDK
14 / 18
Candidate Model | Architecture | Params | QIDK Latency | FPS | Keypoint AP | Selection Status
YOLOv8n-Pose (Nano) | C2f-Pose-Nano | 3.3M | 12.1 ms | 82.6 FPS | 64.0% AP | SELECTED (Unified Pose)
MoveNet Lightning | MobileNetV2 | 2.5M | 7.5 ms | 133.3 FPS | 63.8% AP | Alternative (Ultra-Fast)
YOLOv8s-Pose (Small) | C2f-Pose-Small | 11.6M | 19.5 ms | 51.2 FPS | 69.2% AP | High-Precision Candidate
PRIMARY SELECTION: YOLOv8n-Pose
• Unified Detection & Pose: Combines target localization and 2D keypoint regression in one forward pass, avoiding separate detection overhead.
• Perspective Invariance: Highly resilient to varying aerial camera pitch angles and scale changes during drone descent.
3D GRASP SYNTHESIS INTEGRATION
• PnP / SVD Grasp Solver: Fuses YOLOv8n-Pose keypoints with the FastDepth metric map, solving Perspective-n-Point in <1.5 ms on CPU.
• MoveNet Fallback: MoveNet Lightning (7.5ms) remains available as a lightweight fallback for fast single-object tracking.

## Slide 15
INTEGRATION & DEPLOYMENT // BASELINE
Pipeline Integration: Initial Version
15 / 18
Stage | Model | Precision / I/O | Input | NPU Time (in app) | Stage Total | Observation
Depth | DA-V2 Small | Float, FloatTensor | 392² | 28 ms | 31 ms | Float math on HTP
Segmentation | YOLOv8n-Seg | Float, FloatTensor | 640² | 110 ms | 117 ms | Main bottleneck
Pose + Pipeline | Geometric PCA | CPU | masks + depth | <1 ms | 147 ms | 6.6 FPS end-to-end
BASELINE RESULT: 6.6 FPS (147 ms / frame)
• Measured on QIDK SM8650: 30 s live-camera run, 124 frames, pipeline 141–154 ms per frame; far below the 30 FPS control-loop target.
• First working version: Depth Anything V2 Small + YOLOv8n-Seg in float, depth and seg dispatched in parallel, PCA-based 6-DoF pose on CPU (<1 ms).
• Before that: ViT-L depth (682 MB DLC) + YOLOv8x-Seg (143 MB) ran out of DSP memory when run together.
BOTTLENECKS IDENTIFIED
• Float tensors over JNI: FloatTensor API costs ~15 ms per model per frame in conversion alone.
• Seg decoding bug: CHW data fed to an NHWC model: only 336 of 1344 anchors decoded correctly.
• UI-thread rendering: Per-pixel mask drawing and bitmap building on the UI thread; camera stalls with no recovery.

## Slide 16
INTEGRATION & DEPLOYMENT // OPTIMIZED
Pipeline Integration: Optimised Version
16 / 18
App Variant | Depth (DA-V2 S) | Seg (YOLOv8n) | Camera | Displayed FPS | Pipeline Latency | NPU depth / seg
QIDK FPS | 280², W8A8 | 384², W8A8 | 640×480 @60 | 60.0 (min 59.8) | 7.8 ms | 3.3 / 0.5 ms
QIDK Balance | 392², W8A8 | 640², W8A8 | 640×480 @30 | 30.0 (min 29.3) | 20.1 ms | 6.0 / 1.1 ms
QIDK Quality | 518², W8A8 | 640², W8A16 | 1280×720 @30 | 30.0 (min 29.7) | 29.2 ms | 12.9 / 2.8 ms
OPTIMISATIONS APPLIED
• Quantization: INT8 per-channel weights, 32-bit bias, NHWC-correct calibration; W8A16 for Quality seg.
• Zero-conversion I/O: SNPE TF8/TF16 user buffers in each tensor's native encoding instead of FloatTensor.
• Concurrency: Depth and seg run in parallel on the HTP; overlays built off the UI thread with triple buffering; camera stall watchdog.
RESULT vs BASELINE (measured on QIDK)
• Latency: 147 ms → 20.1 ms (Balance, 7.3x) and 7.8 ms (FPS, 19x).
• Frame rate: 6.6 → 60 FPS (FPS mode); Balance and Quality hold the 30 FPS camera rate with headroom.
• Method: 30 s live runs per app; NPU times from snpe-net-run (100 inferences, burst profile).

## Slide 17
PROJECT ROADMAP // FUTURE TARGETS
Future Targets: Dataset Testing & Accuracy Optimization
Rigorous benchmarking against provided target dataset and progressive accuracy enhancement
17 / 18
TARGET 01
Testing Against Given Dataset
• Dataset Ingestion: Evaluate the complete vision pipeline against the project's designated aerial manipulation dataset and physical lab ground truth.
• Realistic Flight Conditions: Subject models to operational flight stressors: drone hover vibration, varying ambient lighting, oblique camera angles, and ground texture clutter.
• Multi-Modal Alignment: Verify temporal synchronization between RGB camera frames, depth maps, and ground truth 6-DoF grasp annotations.
TARGET 02
Determining Empirical Accuracy
• Quantitative Metric Audit: Measure exact empirical performance across all pipeline stages:
• Depth: AbsRel error, RMSE (m), and inlier threshold (δ < 1.25).
• Segmentation: Mask mAP@50-95 and boundary mIoU.
• Pose: 3D Euclidean position error (mm) and rotational error (deg).
• Failure Mode Breakdown: Identify edge clipping, keypoint occlusion, and false-positive detections under rapid UAV motion.
• Compute Baseline: Profile actual NPU memory bandwidth, thermal stability, and frame latency on physical QIDK hardware.
TARGET 03
Improving Pipeline Accuracy
• Domain-Specific Fine-Tuning: Fine-tune candidate backbones on domain-specific aerial grasp datasets to increase object affordance recall.
• Cross-Modal Boundary Refinement: Fuse YOLOv8 instance contours with FastDepth maps to eliminate depth edge-bleeding and sharpen 3D contact point estimates.
• Temporal Filtering (EKF): Integrate Extended Kalman Filtering across successive frames to filter pose jitter and ensure smooth closed-loop robotic arm trajectory execution.

## Slide 18
CONCLUSION & OUTLOOK
Summary & Project Milestones
Current progress and forward roadmap towards autonomous aerial grasping
18 / 18
MILESTONE COMPLETED
Model Exploration & Benchmarking
• Validated Architectures: Benchmarked candidate models across Depth, Segmentation, and Pose using Qualcomm AI Hub targets.
• Deployed Models: Depth Anything V2 Small (3.3–12.9 ms NPU), YOLOv8n-Seg (0.5–2.8 ms NPU), geometric PCA 6-DoF pose on CPU.
• Pipeline Measured: 60 FPS (FPS mode) and 30 FPS (Balance / Quality) on the QIDK, up from 6.6 FPS baseline.
COMPLETED
Edge Compilation & IPC Integration
• Hexagon NPU Compilation (done): ONNX → DLC, INT8/W8A16 quantization and offline HTP cache for SM8650.
• Zero-Copy Ring Buffer: Implementing POSIX shared memory ring buffers for decoupled multi-stage communication.
• Sensor Calibration: Calibrating camera distortion parameters for 2D-to-3D keypoint de-projection.
TARGET DEMO
Closed-Loop Aerial Grasping
• Hardware-in-the-Loop: Deploy and validate integrated pipeline on the physical Qualcomm QIDK developer board.
• End-Effector Grasp Test: Demonstrate autonomous detection, 3D pose alignment, and physical pick-and-place in lab mock-up.
• Control Jitter Robustness: Verify tracking stability under simulated UAV hover vibration and attitude perturbations.